## Slide 1
OralTrack
Smart Oral Hygiene Monitoring System
Track. Improve. Optimize.
Name: Ashish Verma Student ID: 2024PEB5060
MNIT Jaipur, ECE Department

## Slide 2
Project Overview
Project Name: Smart Oral Hygiene Monitoring System
Objective: To help users brush for the optimal time and track their progress over time.
Key Features:
  Timer starts when a user picks up their toothbrush.
  Tracks brushing time and logs data for analysis for the past 30 days.
  The web interface enables users to edit their profile information.
  Additional features: UVC LED light and buzzer control from the web.

## Slide 3
Problem Statement
Challenges in Oral Hygiene:
  Most people don’t brush for the minimum* recommended 2 minutes.
  Lack of awareness of brushing habits and their impact.
Solution Offered:
  Real-time brushing monitoring and feedback.
  Easy access to brushing history for behaviour improvement.
  Promotes ADA recommendations for better dental health. *Minimum does not necessarily mean optimal..

## Slide 4
Research References
ADA Recommendation
Brush for at least for two minutes twice daily with a soft-bristled toothbrush.
Study Insights-1
Brushing for 120 seconds removes 26% more plaque than 45 seconds.
Study Insights-2
180 seconds removes 55% more plaque than 45 seconds.
Notes: https://www.ada.org/resources/ada-library/oral-health-topics/toothbrushes https://www.jacksonavedental.com/post/how-long-you-should-brush-your-teeth

## Slide 5
Features
1
Tracks Brushing Duration
Tracks brushing duration for two users.
2
Sends Data to Server
Sends brushing data to the NODEMCU server.
Graph for past 30 days
3
Real-Time Feedback
Displays real-time brushing timer on OLED
Feedback from buzzer.
4
Configurable Settings from Web
User names.
Adjusting timer for each user.
Controlling Buzzer and UVC LED.

## Slide 6
Hardware Overview
MCUs
STM32F051 and
NODEMCU (ESP8266)
Sensors
Two IR sensors for detecting brush pick-up and placement
Display
0.96-inch OLED for real-time feedback
Additional
Buzzer for feedback

## Slide 7
Software Features
STM32
  GPIOs: For sensor inputs.
  I2C: Interface with OLED display (SSD1366 library).
  Timer-1: Core timer for brushing duration.(16 bit)
  EEPROM: Stores the user information and brushing logs.
  UART: Communication between STM32 and NODEMCU (interrupt mode).
  My Custom Libraries: Created for UART and EEPROM functions.
NodeMCU:
  Mode Used: Station mode.
  Getting date & time from Internet.(NTPClient.h library)
Notes: 256 Kbyte of flash memory Main flash memory block: Up to 64 Kword (64 K × 32 bits)

## Slide 8
Advantages
1
Healthier Brushing Habits
Promotes healthier brushing habits.
2
User-Friendly Interface
User-friendly interface and real-time feedback.
3
Data-Driven Progress
Data-driven progress tracking.
4
Smart Design
Compact, multifunctional design.

## Slide 9
Disadvantages
1
No confirmation
Did user really brush their teeth after picking their brush?
2
Optimum for small family
OLED display can show data for 4 members

## Slide 10
Demo and Results
Home Screen
Timer Running for Users
Time Completed

## Slide 11
Demo and Results
Web Controls
Screenshots of the web interface
Brushing History
Screenshots of the web interface and brushing history log.

## Slide 12
Conclusion
1
Summary
OralTrack helps users improve their oral hygiene by tracking their brushing habits.
2
Future Scope P-1
Making a smart brush which will be able to measure the brushing speed also confirm the brushing after picking. Integration the system with mobile apps for better accessibility.
3
Future Scope P-2
AI-driven analysis of brushing patterns.